## Slide 1: Innovative Smart Jacket for Chennai Metro Workers Using IoT
PREPARED BY: GUIDED BY:
ABICIYA.M(212921106002) MR . SANTHOSH.S M.E.,
KAVIYA.K(212921106040) Assistant Professor/ECE
GOPIKA.S(212921106020)

## Slide 2: Abstract:
The IoT-Enabled Smart Safety Jacket for Chennai Metro Workers is designed to enhance worker safety by continuously monitoring health parameters and environmental conditions using the NodeMCU ESP8266 microcontroller.
The jacket is equipped with multiple sensors, including a heart rate sensor, temperature sensor, gas sensor, and pressure sensor, which collect real-time data and transmit it to the Blynk mobile application for remote monitoring.
If any parameter exceeds a predefined safety threshold, an instant alert is triggered via a buzzer, and a real-time notification is sent to the Blynk app, enabling immediate action to prevent accidents or health risks.
The system ensures quick response to hazardous conditions such as abnormal heart rate, excessive heat, toxic gas leaks, or sudden pressure changes. With its wireless connectivity, real-time monitoring, and automated alerts, this smart jacket provides an efficient IoT-based safety solution for metro workers operating in high-risk environments.
It helps supervisors ensure worker well-being, reduces workplace hazards, and enhances overall operational safety in metro construction and maintenance sites

## Slide 3: INTRODUCTION:-
Ensuring the safety and well-being of metro workers is crucial, especially in high-risk environments such as underground tunnels and construction sites.
The IoT-Enabled Smart Safety Jacket is an innovative solution designed to provide real-time health monitoring and hazard detection using advanced sensor technology and IoT connectivity.
Developed using the NodeMCU ESP8266 microcontroller, this smart jacket integrates sensors to measure heart rate, body temperature, gas levels, and pressure, continuously transmitting data to the Blynk mobile application for remote monitoring.
By leveraging IoT, the system enables supervisors to track worker health and environmental conditions in real time. If any sensor value exceeds the safety threshold, an instant alert is triggered through a buzzer, and a notification is sent via the Blynk app to facilitate quick emergency response. This innovative approach enhances workplace safety, reduces risks, and ensures proactive hazard management, making it an essential safety solution for Chennai Metro workers.

## Slide 4: Objective
Monitor worker health using IoT sensors.
Detect hazardous gases and pressure changes.
Send real-time alerts via buzzer and Blynk app.
Ensure safety in metro work environments.

## Slide 5: LITERATURE SURVEY
S.no | Title | Author | Content
1 | IOT based Coal Mine Safety Monitoring And Alerting System | Manohara K M, Nayan Chandan D C, Pooja S V, Sonika P, Ravikumar K I Year:2021 | Coal mines are one of the most important and industries in the country, as they are used as fuel in the steel and cement industries to extract iron from the stone and create cement. Every parameter, such as methane gas, high temperature, fire incidents, etc., should be regularly checked in the underground mining business. Due to the complexity of the mining environment and the variety of activities performed in coal mines, it is important to monitor the working environment. To address this issue, there is a system that monitors basic safety measures and regulates many restrictions on coal mines, such as gas leaks, temperature and humidity conditions, and fire sensor. All the sensors are assembled into a single unit and then placed in a coal mine.

## Slide 6
S.no | Title | Author | content
2 | Coal Mine Safety Monitoring and Alerting System with Smart Helmet | Mangesh Rudrawar, Shivam Sharma, Madhuri Thakur, Vivek Kadam Year: 2022 | Traditional monitoring systems in coal mines are difficult to install, hazardous, and difficult to power. Because of the complexity of the mining environment and the wide range of operations performed in coal mines, it is vital to monitor and maintain the parameters in the background t increase the efficiency and safety of mineworkers. As a result, traditional monitoring methods cannot be relied on to ensure coal workers’ safety. This research represents a ZigBee-based wireless monitoring system using a smart helmet.

## Slide 7
S.no | Title | Author | Content
3 | Safety Monitoring System in Coal Mine Using IoT | Sathishkumar N1 , Manoj A M2 , Muniraj K2 , Naveenkumar M2 , Praveen C2 Year:2022 | The key abstract is to use IoT to incorporate a coal mine safety monitoring system. The extraction of coal from the field is known as coal mining. Coal is used as a fuel in the steel and cement industry to extract iron from ore and to manufacture cement. Every parameter in the underground mining industry must be controlled on a regular basis, including methane gas, high temperatures, fire incidents, and so on. The level of safety in coal mines is still poor, resulting in fatalities. A coal mineshaft salvage action is profoundly perilous because of various elements.

## Slide 8
S.no | Title | Author | Content
4 | A SMART HELMET FOR COAL MINERS | V. Sai Prasanna Kumar, M. Shiva Rama Krishna, Dr K. Shambavi YEAR:2022 | This paper uses LoRa communication technologyand GSM to send and receive information, Arduino to process the information. sensorssuch as MQ02, DHT11, IR sensor, vibration sensor to get the parameters. The mainobjective of using LoRa communication is to make sure the communication is strongeven in the longer ranges where Zigbee runs out of range. The range provided by Zigbeeis up to 300 meters whereas the range for LoRa can be up to 5 kms depending on thetraffic in that area. The Arduino microcontroller processes the information received from the sensors and sends the information via LoRa and GSM. proper action can betaken by the control room and the workers can be evacuated or the conditions can beimproved

## Slide 9
S.no | Title | Author | Content
5 | IOT BASED SMART HELMET FOR UNSAFE EVENT DETECTION FOR MINING INDUSTRY | Rupali Arjun Shejule, Vijaya Rahul Pawar YEAR:2017 | The first is the fixation level of the risky gasses, for example, CO, SO2, NO2 and particulate issue. The well being head protectors do not have any innovation added there to inform excavators when a kindred digger has experienced an unsafe occasion. Lately, gathering advancement has assumed an important part within the territory of mine applications. The writing on mines innovation is accessible however exceptionally restricted. This project mainly focuses on a mine supervising system monitor using IOT. Our project aims at developing a wireless sensor networks, realized real time surveillance with early-warning intelligence on harmful gases in mining area and used GPRS to monitor potential safety problems in coal production using a IOT technology. In addition, thereto it gives alarm sound using buzzer when any harmful gas is detected and person not wear helmet. In the LCD the data is displayed.

## Slide 10: EXISTING SYSTEM:
The existing safety systems for metro workers rely on basic monitoring techniques, where sensor data such as heart rate, temperature, gas levels, and pressure are displayed only on an LCD screen.
Workers or supervisors must manually check the readings, making real-time monitoring and quick emergency response difficult.
These systems lack IoT connectivity, meaning there are no remote alerts, mobile notifications, or automated warnings when a hazardous condition occurs.
This limitation increases the risk of delayed action in emergencies, reducing overall worker safety. Without IoT integration, the system is less efficient in preventing accidents and ensuring proactive safety measures in metro work environments.

## Slide 11: Drawbacks
No remote monitoring as data is only visible on an LCD.
Delayed emergency response due to lack of real-time alerts.
Limited accessibility since supervisors cannot track worker health remotely.
Higher risk of accidents due to absence of automated alerts.

## Slide 12: Proposed system:
The proposed system introduces an IoT-enabled smart safety jacket for Chennai metro workers, integrating NodeMCU ESP8266 with multiple sensors to monitor heart rate, temperature, gas levels, and pressure in real time.
Unlike the existing system, this solution transmits sensor data to the Blynk mobile application, enabling remote monitoring by supervisors.
If any parameter exceeds the safety threshold, the system triggers an instant buzzer alarm and sends a real-time notification to the mobile app, ensuring quick emergency response.
This automated alert system enhances worker safety, reduces risks, and improves overall efficiency in metro work environments by enabling proactive hazard detection and immediate action.

## Slide 13: BLOCK DIAGRAM:
Nodemcu 8266
Controller
DHT11 SENSOR
POISONOUS GAS Sensor
PRESSURE SENSOR
HEARTBEAT
SENSOR
IOT
Power Supply
Cloud
BUZZER

## Slide 14: Hardware used
NodeMCU Controller
POISONOUS sensor
HEARBEAT Sensor
DHT11 Sensor
PRESSURE Sensor
Wifi Module
LCD Display

## Slide 15: Software Used:
Arduino IDE
Embedded C

## Slide 16: Reference
[1] Geetha, A.. (2014). Intelligent helmet for coal miners with voice over ZigBee andenvironmental monitoring. World Applied Sciences Journal. 20. 2328-2330. 10.5829/idosi.mejsr.2014.20.12.332.
[2] R. K. Kodali and B. S. Sarjerao, ”A low cost smart irrigation system using MQTT protocol,” 2017 IEEE Region 10 Symposium (TENSYMP), Cochin, India, 2017, pp. 1-5, doi: 10.1109/TENCONSpring.2017.8070095.
[3] R. K. Kodali and A. Sahu, ”An IoT based soil moisture monitoring on Losant platform,” 2016 2nd International Conference on Contemporary Computing and Informatics (IC3I), Greater Noida, India, 2016, pp. 764- 768, doi: 10.1109/IC3I.2016.7918063.
[4] R. K. Kodali and K. S. Mahesh, ”Low cost ambient monitoring using ESP8266,” 2016 2nd International Conference on Contemporary Computing and Informatics (IC3I), Greater Noida, India, 2016, pp. 779-782, doi: 10.1109/IC3I.2016.7918788.
[5] P. Vamsikrishna, Sonti Dinesh Kumar, Shaik Riyaz Hussain and K. Rama Naidu, ”Raspberry PI controlled SMS-Update-Notification (Sun) system,” 2015 IEEE International Conference on Electrical, Computer and Communication Technologies (ICECCT), Coimbatore, India, 2015, pp. 1-4, doi: 10.1109/ICECCT.2015.7226113.

## Slide 17
[6] Salankar, Pranoti Anandrao and S. Suresh. “Zigbee Based Underground Mines Parameter Monitoring System for Rescue and Protection.” IOSR journal of VLSI and Signal Processing 4 (2014): 32-36.
[7] M. Ali, J. H. Alfonsus Vlaskamp, N. N. Eddin, B. Falconer and C. Oram, ”Technical development and socioeconomic implications of the Raspberry Pi as a learning tool in developing countries,” 2013 5th Computer Science and Electronic Engineering Conference (CEEC), Colchester, UK, 2013, pp. 103-108, doi: 10.1109/CEEC.2013.6659454.
[8] H. Li, ”Research on safety monitoring system of workers in dangerous operation area of port,” 2017 4th International Conference on Transportation Information and Safety (ICTIS), Banff, AB, Canada, 2017, pp. 400-408, doi: 10.1109/ICTIS.2017.8047796.
[9] A. Mishra, S. Malhotra, Ruchira, P. choudekar and H. P. Singh, ”Real Time Monitoring & Analyzation Of Hazardous Parameters In Underground Coal Mines Using Intelligent Helmet System,” 2018 4th International Conference on Computational Intelligence & Communication Technology (CICT), Ghaziabad, India, 2018, pp. 1-5, doi: 10.1109/CIACT.2018.8480177.
[10] V. Thirumala, T. Verma and S. Gupta, ”Injury analysis of mine workers: A case study,” 2017 IEEE International Conference on Industrial Engineering and Engineering Management (IEEM), Singapore, 2017, pp. 269-273, doi: 10.1109/IEEM.2017.8289894.

## Slide 18: Conclusion
The Smart Jacket for Chennai Metro Workers enhances safety and efficiency through IoT-based monitoring. It features GPS tracking, environmental sensors, and emergency alerts. This design ensures real-time protection and better working conditions. Future improvements can focus on battery optimization and AI integration for predictive safety measures.

## Slide 19: Thank you